XBee Acquisition Network Design Notes
# Introduction
This describes a project to build a support base for a data acquisition network in which the communication between nodes of the network uses XBee devices in Zigbee mode.
The document describes the various design parameters and decisions, and documents the protocols and interfaces between components.
The concept involves a Linux based coordinator processor, referred to as the base station, intended to be a small headless platform such as the Raspberry Pi, BeagleBone or similar. By means of a background base station process this provides a control, configuration and collection point for incoming data via an attached an XBee in coordinator mode. It also provides a network interface to a Linux, OS/X or Windows based user interface program on the same or different machine.
The remote nodes provide the data acquisition facilities. The remote nodes can be of two types: XBee end devices and XBee routers. The latter must be always on and powered with an uninterruptible supply, while the former may be battery operated and use sleep states extensively to conserve power. As the XBee is capable of performing a small number of analogue measurements and provides basic digital I/O, it can operate as a standalone device. Alternatively, and preferably for flexibility, it can operate in conjunction with a small microcontroller. The latter configuration has a number of advantages in that each can monitor the other and provide some additional fault recovery functionality, such as remote reset, firmware uploads for the microcontroller, watchdog timer reset and remote configuration of the XBee.
Most remote nodes will use battery operation and thus they will make use of various XBee sleep states. Most modern microcontrollers can also use sleep states. As the microcontroller is likely to wake from sleep on various local events, it can also wake the XBee when transmission is required.
A number of items of software are developed for this work:
1. Base station program for monitoring, data collection and buffering, and interface to an external control program.
2. Data acquisition and control program for the remote node microcontroller.
3. Bootloader for the remote node microcontroller to allow firmware uploads.
4. External GUI program for connection to the base station over the Internet or local LAN, for monitoring, control and data access.
The remote node for the watermeter is described in another document.
# Xbee Setup
The XBee can be setup initially with the Digi X-CTU tool. This is available for Windows, OS/X and Linux http://www.digi.com/products/xbee-rf-solutions/xctu-software/xctu.
In Linux, the downloaded file has a .run suffix. Make executable and execute as root, eg

$ chmod +x 40002881_B.run
$ sudo ./40002881_B.run
If it is installed to the default directory /opt/Digi, it can be run as:

$ /opt/Digi/XCTU-NG/app
Connect an XBee to a USB port. It will normally then appear as /dev/ttyUSB0 (although the number will be higher if other devices or disk drives have already been attached). Perform a search for the attached XBee. If not found, widen the search to different serial settings. The XBee cannot communicate its serial settings so a search must be done.
## Network Setup
1. If the XBees have been set with the correct network parameters as described below, install the coordinator on a PC with X-CTU installed. Check that it is recognised and the parameters are correct. The coordinator should have
2. Connect the router Xbees to a suitable power source. Each of these should start up (connect to the network) after a few seconds. If LEDs are present, the “associate” LED (pin 15) should blink at a rate twice per second once the XBee has joined the network.
3. In X-CTU clink on the “Discover Radio Nodes” button for the coordinator entry. All nodes should be found.
## XBee Settings
These are the settings available from the X-CTU tool.
The network PAN ID is selected as 55 for this system. This is set in all XBees to be used in the network.
### Sleep Time
The coordinator and routers are to be set to never sleep. These must always be powered on by an uninterruptible power source. The end devices are required to sleep to conserve battery power but may be forced permanently awake via the SLEEP_RQ pin being held low.
The sleep time setting on the coordinator and routers refers to the maximum time that end devices are expected to sleep. If an end device does not respond during this time it is purged from the list of child devices. The setting therefore must be a larger value than the end device setting to ensure that the end device remains in the child table and is not expired. Any end point should wake at least once per day.
The sleep setting on end devices will be pin sleep or cyclic sleep plus pin sleep. For power reduction the sleep time must be as long as possible. For safety the cyclic sleep setting plus pin wake should be used to ensure the XBee wakes up regularly to refresh the network connectivity. The sleep options are set to allow a sleep holdoff time to be defined and to enable extended sleeping.
When the end device XBee wakes, an setting can be used to allow it to remain awake for a fixed period to allow remote devices and processes to send any pending messages. The end device XBee must receive and respond to these messages before sleeping. The setting only applies to cyclic sleep mode and not for pin sleep mode, although it appears to be active for pin wake when pin plus cyclic sleep mode is used.
### Router
- NJ – Node join time. If less than FF the device assumes the network doesn't allow joining and attempts to rejoin. This allows it to join a network with the same PAN ID. If this fails, or NJ is FF, it joins by association.
- PAN ID – set to the selected PAN ID of the coordinator. If set to zero, the XBee will pick up the PAN ID from the coordinator (as long as only one coordinator is around).
- NW = 1. Network Watchdog Timeout in minutes to cause the XBee to check for a coordinator and leave if not found (0 is disabled). This is normally set to a higher value.
- JV = 1. Channel verification causes the XBee router to check for a coordinator on power up and search for one if not found.
- JN = 1. Join notification causes the XBee to send a node identifier packet on power up. This is needed to ensure it is entered into the software table.
- BD = 5. Set the baud rate to 38400.
- D7 = 1 Enable CTS flow control.
- D6 = 1 Enable RTS flow control.
- AP = 1 Use API mode without break characters.
- SM = 0. Set the sleep mode to disable.
- SP = 0xAF0. Set the sleep period to the maximum 28 seconds.
- SN = 0xB60. Cyclic sleep periods, up to FFFF. Set to just over 1 day.
- PR = 0x1FBF. Set the pullup resistors to exclude CTS (which is an output) and SLEEP_RQ which needs an external pull down of large value.
### End Point
- PAN ID – set to the selected PAN ID of the coordinator. If set to zero, the XBee will pick up the PAN ID from the coordinator (as long as only one coordinator is around).
- NJ – Node join time. If less than FF the device assumes the network doesn't allow joining and attempts to rejoin. This allows it to join a network with the same PAN ID. If this fails, or NJ is FF, it joins by association.
- NW = 1. Network Watchdog Timeout in minutes to cause the XBee to check for a coordinator and leave if not found (0 is disabled). This is normally set to a higher value.
- JN = 1. Join notification causes the XBee to send a node identifier packet on power up. This is needed to ensure it is entered into the software table.
- MP – Parent address (0 for coordinator, or address of router).
- NT – Node discovery backoff time (3C about 6 seconds).
- NO – Node discovery options (3).
- BD = 5. Set the baud rate to 38400.
- D7 = 1 Enable CTS flow control.
- D6 = 1 Enable RTS flow control.
- AP = 1 Use API mode without break characters.
- SM = 5. Set the sleep mode to cyclic sleep plus pin wake.
- SP = 0xAF0. Set the sleep period to the maximum 28 seconds.
- SN = 0xB40. Cyclic sleep periods, up to FFFF. Set to about 1 day.
- ST = 0x1F4. Set the sleep holdoff time to 0.5 seconds. Only for cyclic sleep.
- SO = 6. Enable extended sleep (4) and sleep for full ST time (2).
- PR = 0x1FBF. Set the pullup resistors to exclude CTS (which is an output) and SLEEP_RQ which needs an external pull down of large value.
### Coordinator
- ID – set to the selected 16 bit PAN ID. If set to zero, the XBee will pick a random number.
- SC – Scan channels bitmask for up to 16 channels. Coordinator will select a channel when forming the network. Defaults to FFFF.
- SD – Scan duration. How long the coordinator spends scanning for PAN ID or energy scan. The setting is an exponent (3) in units of 15.3ms per channel.
- ZS – Zigbee stack profile. Same on all devices on the network. This is related to specialised applications. Normally set to 0.
- NJ – Node join time. Time allowed for remote nodes to join. If set to FF it will have no time limit. After the limit has expired, remote nodes are unable to rejoin until the coordinator is reset or NJ is changed.
- OP – Operating PAN ID (should match the nonzero value in ID).
- OI – Operating 16 bit PAN ID.
- CH – Operating channel.
- NC – Number of children remaining (routers and end-points directly accessing the coordinator).
- SH, SL – Serial Number high and low.
- MY – 16 bit network address (0 for coordinator).
- DH, DL – Destination address (0000 FFFF for coordinator).
- NI – Node identifier ASCII name.
- NH – Maximum number of hops. Default 1E is about 1.6 seconds, 8 hops
- BH – Broadcast radius. For maximum number of hops set to 0.
- AR – Aggregate routing notification. Time between consecutive aggregate broadcasts.
- DD – Device type identifier (30000).
- NT – Node discovery backoff time (FF).
- NO – Node discovery options (3).
- NP – Maximum number of RF payload bytes (FF).
- CR – PAN conflict threshold (3). Not mentioned in documentation.
- BD = 5. Set the baud rate to 38400.
- D7 = 1 Enable CTS flow control.
- D6 = 1 Enable RTS flow control.
- AP = 1 Use API mode without break characters.
- SM = 0. Set the sleep mode to disable.
- SP = 0xAF0. Set the sleep period to the maximum 28 seconds.
- SN = 0xB60. Cyclic sleep periods, up to FFFF. Set to just over 1 day.
- PR = 0x1FBF. Set the pullup resistors to exclude CTS (which is an output) and SLEEP_RQ which needs an external pull down of large value.
# Base Station
The base station processor being used for this project may be almost any Linux based PC or processor board. This interfaces to the local WiFi or Ethernet LAN to allow external control and data transmission. It may use a HDD or SD card for data buffering.
## Configuration
The configuration of the base station processor depends rather on its hardware features. A full PC needs little configuration as it will be able to respond to almost any load demand from the network. A small processor board however may need some work to improve performance.
## Software
It is intended that the processor be set to start a background monitoring process to control the network, gather incoming data, pass it to storage buffers and interact with an Internet GUI control and display program. The program is written in C and uses libxbee for XBee support.
The requirements for the program are:
1. On startup, initialise an Internet socket for attachment by an external user interface program. This socket shall listen on TCP port 58532.
2. For each remote node in the table, make a data connection on which incoming data for each remote node will be received.
3. Create an “Identify” connection to receive identification packets from remote nodes when they power on or join the network. Note: all stand-alone XBee nodes should have the Join Notification setting enabled to allow new nodes to identify themselves to the network. The software in the XBee-microcontroller combo shall force the sending of the Identify packet when powering up.
4. Send out an XBee Node Discovery command via the attached coordinator XBee to query all remote nodes in the network. From the responses build a table of node information.
5. On receiving Identify packets the program shall check against the existing table and add the remote node if it is not already present.
## Internet Interface
Commands received over the Internet connection from an external user interface program have the following format:
1-byte length, 1-character command, 1-byte row number, arbitrary parameters (0-255)
For transmission to remote nodes, the row number points to a table entry with the node information and connections.
The commands (n represents the remote node's row number) are:
- N - return the number of rows in the table
- In - return the textual and numerical information in the node entry.
- Sn... - send a string to the remote node over its data connection.
- s - ask for any response returned by the remote node to an S command on the data connection. A value of zero returned as the first character indicates that a response had not been received. The first character of a valid response will be an ASCII 'S' to indicate that a response was received.
- Rn... - send a remote AT command plus its parameters to the remote node.
- r - ask for any response returned by the remote node to an R command on the data connection. A value of zero returned as the first character indicates that a response had not been received. The first character of a valid response will be an ASCII 'R' to indicate that a response was received.
- Ln... - send a local AT command plus its parameters to the attached coordinator XBee.
- l - ask for any response returned by the remote node to an L command on the data connection. A value of zero returned as the first character indicates that a response had not been received. The first character of a valid response will be an ASCII 'L' to indicate that a response was received.
- X – close down the XBee network and, after a 20 second delay, restart it. This has presented a number of issues with remote nodes not being recognised, and is not recommended to be used.
- Q – close down the selected remote node data, I/O and command connections, and rebuild them.
- D – Delete a selected remote node from the node table.
The convention used is upper case letters to represent a direct command and a lower case letter used to request any response.
# Remote Nodes
These devices shall use sleep modes to reduce power drain to a minimum. The XBee can be placed in “pin sleep” and await the microcontroller action on a specific pin to wake it up. Alternately it can be made to wake periodically so that in the event of a non-responding microcontroller, it can force the latter to be reset. The microcontroller can also force a hardware reset on the XBee if the latter fails to respond. The microcontroller shall be placed in a sleep mode also.
## Sleep Modes
The XBee shall be set to Sleep Mode 1 (pin sleep). This allows the XBee to sleep until awoken by the action of the SLEEP_RQ pin, controlled by the microcontroller.
Note the controller and all routers must have their sleep options set to the same value or greater to ensure they retain end device messages until the latter awakes. These sleep options refer to the time allowed for end devices to remain asleep (the coordinator and routers never sleep).
The microcontroller shall be placed in sleep mode until data becomes available or until the XBee wakes it. The XBee ON/SLEEP output can be used to a wakeup the microcontroller. An AVR microcontroller shall use the power save sleep mode if the timer/counter is to be used, otherwise power down mode shall be used. Both can be woken with a pin change interrupt.
### Configuration
When configuration of the XBee is to be done, a message shall be sent to the XBee to perform the appropriate action. This must occur when the XBee is woken by the remote node microcontroller.
To account for the case where the AVR hasn't been given the ability to change the XBee sleep state, an XBee command will need to be sent by the controller to change the sleep mode to pin sleep. The XBee will then need to have its SLEEP_RQ pin grounded to ensure that it remains awake indefinitely in this mode. The XBee end devices cannot be set to remain permanently on, and must use one of the sleep modes.
### Bootloader
The need to reset the AVR when activating the bootloader results in the SLEEP_RQ pin of the XBee being forced high during the reset, as all I/O ports on the AVR are changed to inputs. This puts the XBee to sleep and cuts off communication. To overcome this, a 1M or larger resistor is used as a pull-down and the pull-up on the XBee SLEEP_RQ pin is disabled.
# Communication Protocols
On top of the Xbee networking protocol is needed a specific application protocol to communicate between the remote node microcontroller and the base station process. This shall be done by means of a command/response mechanism consisting of a command or response code word possibly followed by data. A code word that doesn't belong to the following list shall result in an error response.
The protocol shall consist of an ASCII command character followed by a string of ASCII hexadecimal characters representing numerical data, or other ASCII characters representing non-numerical data.
## Bootloader
The following commands apply to interaction with the bootloader only.
- : (semicolon). The following data shall be a single record of iHex formatted hexadecimal characters, pairs of which represent a data byte, and having maximum length 16 data bytes. The record types 00 and 01 (end of file) are recognised. Error responses include invalid hex character, checksum, record length and record type.
- Q. Quit the bootloader and enter application program at address zero.
- X. Erase all application memory.
Responses
- Y no error.
- E unspecified error response.
- B out of bounds (bootloader has been asked to write over itself).
- L invalid iHex record length
- H invalid hexadecimal character
- X invalid checksum
- I invalid command (including invalid data where appropriate)
- J a jump to the application has been made from the bootloader.
## Base Station to Remote Node Interactions
As specified above, in the remote node, both the microcontroller and the XBee will sleep. The microcontroller will wake at intervals and will then wake the XBee to check for waiting messages and to send data. Regardless of any data to be sent the base station must receive a message from the remote node and respond. Then the remote node may return to sleep.
For safety the remote node must wait for a limited period of time for a response, and resend the message if no response has been received. The following protocol shall be followed to improve the reliability of communication in the presence of possible errors.
If no response has been received, then the remote node may check the XBee for valid status, to determine if it is still joined to the network. If not, then the XBee shall be restarted. Otherwise the remote node shall return to sleep on the assumption that the network is not responding. Accumulated data shall be retained for subsequent attempts.
## Data Transfer Protocol
A reliable protocol is required to ensure that the collected data is transferred accurately to the system.
If data is transferred correctly, then the old data must be cleared to make room for a new set.
### Protocol
- When the XBee is ready to send, wake up and send a contact message with the data and a checksum.
- Receive an acknowledgement, or negative acknowledgement if data was received in error by the base station.
- If timeout, repeat the contact message until the acknowledgement is received or until three attempts have failed.
- If any other error occurs, resend the data message up to three times.
- On failure send a signal to indicate that the results should be discarded.
- On success, reset the data and send a signal to store the result.
The length of the data field can be inferred from the message length. All fields shall consist of printable ASCII characters for readability and error checking. Because of limited memory in the AVR, the messages shall have limited length.
If the remote gives up, then it shall send a final message stating that it is giving up and will not reset the count. The base station shall then discard the result.
### Error Recovery
Successful error recovery requires careful design. However it is not possible to anticipate all possible errors. These can arise from corruptions in the communications at the Xbee-AVR interface, or in the XBee network itself.
- When a message is transmitted the XBee will return a Tx Status message with a delivery notification.
- It is unlikely that the Tx Status message will be corrupted or missing, but in that case it would be best to assume that delivery occurred and leave any timeouts to the remainder of the protocol. Therefore do not repeat for a corrupted frame and on timeout simply exit.
- Only report a failure if the Tx Status frame was valid and non-delivery was reported.
### Message types
The messages from the XBee contain the data to be sent. xx represents checksum, aa represents data:
1. Original data message 'C' xx xx aa aa … (11 bytes).
2. Repeat message in response to reception errors 'E' xx xx aa aa … (11 bytes).
3. Repeat message in response to a NAK 'N' xx xx aa aa … (11 bytes).
4. Repeat message in response to a timeout 'T' xx xx aa aa … (11 bytes).
5. Remote will abandon the communication attempt 'X' (1 byte).
6. Remote accepts the communication 'A' (1 byte).
7. Debug message 'D' aa aa … (unlimited bytes).
The messages from the system are:
1. Acknowledgement 'A' (1 byte).
2. Negative acknowledgement 'N' (1 byte).
3. Parameter change command 'P' aa aa ... (n+1 bytes).
4. Keep awake until further notice 'W'.
5. Sleep 'S'.
## Parameter Change Command
If a parameter change operation is required, the parameter change command must be transmitted by the base station immediately after the reception of the data command. This will ensure that the operation takes place before the remote node returns to sleep.
The remote node must respond with an acknowledgement of the parameter change command.
## Protocol Interface
The best place for the protocol interface is in the base station. Data can be collected during the protocol exchange and stored ready to pass to the external PC. All that is needed for configuration is the way that data is stored for each sensor.
Data storage shall be made firstly in a global data structure that contains only one result for each of the remotes in the network. Following a signal from a remote that the data transmission is successful, the result will be written to a permanent data file. The temporarily stored datum will be overwritten by subsequent transmissions, therefore if the acknowledgement was not received from the remote, the datum would be lost. To avoid this loss, the old datum shall be written to the file with a marker indicating that its status is dubious.
# Software Development
## Base Station
The base station program is intended to be run on a Linux machine which can range from a single card computer such as the Raspberry Pi to a full PC. Most likely a low to medium range PC can be used as the performance demands would not be very great.
The base station program is not intended to interface to a user. Rather it communicates via an Internet socket with an external user program such as the XBee-GUI program described below.
The program is developed in C and uses only standard POSIX libraries plus the libxbee libraries created by Attie Grande. The latter must be installed in a suitable location and compiled to produce a libxbee.a archive file. If the system install procedure has not been used as described in the libxbee documentation, then libxbee.a must be copied along with the xbee.h file to the base station program source directory. The base station program can then be compiled using “make” to produce a xbee-acqcontrol executable.
When the xbee-acqcontrol program is run from the command line, it produces a one-line output and then waits for responses from the Xbee network and the user interface program. Error messages are printed to the /var/log/syslog file, labelled clearly as originating from the base station program. Typical errors that cause the program to end prematurely might be unable to open a file for printing of remote node results messages. If the debug setting is used when compiling, the program will also print to stdout. If the network is operating correctly messages should be seen from the remote nodes.
Command line options for xbee-acqcontrol are
-d directory to store results file
-P port (default is /dev/ttyUSB0)
-b baudrate (default 38400 baud)
## XBee-GUI
The GUI program is developed in C++ using the QT4 graphical libraries.
### Linux Installation
For Linux use, the following QT4 development libraries should be installed: qt4-designer, qt4-dev-tools, qt4-doc, qt4-qmake.
The program otherwise only uses the standard POSIX libraries.
Build the program with
- qmake
- make clean
- make
### Windows Installation
For development or compilation, download the QT opensource version 4.8.4 for Mingw 4.4 (http://qt-project.org/downloads). Install to its default folder .
Download the Mingw install GUI (http://www.mingw.org/wiki/Getting_Started). Also install to its default folder, as that will be used by default by QT. Copy the source files for XBee-GUI to a folder C:\XBee-GUI. From the start menu, open the QT 4.8.4 command prompt in the QT by Digia v4.8.4 entry. In the window, change directory to C:\XBee-GUI and issue the commands:
- qmake
- make clean
- make
The executable will appear in the “release” folder. To make it distributable, add copies of the following files found in the MinGW\bin and QT\4.8.4\bin folders:
- libgcc_s_dw2-1.dll
- libstdc++-6.dll
- mingwm10.dll
- QtCore4.dll
- QtGui4.dll
- QtNetwork4.dll
The resulting set of files can then be bundled into a zip file for distribution and should run on any Windows 7 installation without additional actions needed.
## Remote Node Firmware Arduino Development
For development of code on the remote node microcontroller it may be sufficient to make use of the Arduino IDE without the upload feature. This needs to be modified to ensure that the Intel iHex formatted binary file appears in an accessible place and is not deleted. To the Arduino IDE preferences configuration file (this file can be found as described in http://arduino.cc/en/Hacking/Preferences) add the following lines:
export.delete_target_folder=false
build.path=build
The former prevents deletion of the generated build files, and the latter places all build files into a local directory called “build”.
Once the hex file is available it can be uploaded using the XBee-GUI program.
## Bootloader for ATMega
The bootloader shall sit in the allocated bootloader area of memory. On reset the microcontroller will start in this region automatically. The bootloader shall test the XBee bootloader output. If active, it shall wait for commands on the data channel to clear the Flash memory program area and to program pages of instructions. Otherwise it shall jump to the start of application code.
The bootloader must perform necessary hardware initialisation. For AVR devices this means disabling the watchdog timer (which remains enabled after a hardware reset).
The firmware data format shall be Intel iHex, which is compatible with many linker outputs. Reception of an iHex line will result in a block of data being programmed to Flash. Since an iHex line starts with a colon, that character will be taken as a command to program the line. A small number of other commands may be used to allow some additional functionality if space permits. The maximum length of a line shall be 16 byte of data.
As mentioned earlier, the bootloader will test the chosen bootloader output pin of the XBee at intervals and will jump to the application area if it is active.
Once a command to load memory has been received, the relevant memory block will be erased. A lock variable shall be set to indicate that this has happened as it must not be done again for the same block.
Because of the limited memory in the bootloader region, code shall be optimised for size.
The serial interface with the XBee should support flow control to take advantage of buffering in the XBee itself. This allow the bootloader to perform the lengthy erase and write operations with reduced probability of loss of frames. The protocol used in the base program should repeat frames if a negative acknowledgement is received.
The Bootloader requires close to 2K of FLASH, so the selected microcontroller will need to support this.
## Bootloader for ATTiny and ATMega48
These AVRs do not have a separate bootloader region and therefore the process of programming the FLASH becomes complicated.
## Remote Node Firmware General
The microcontroller application shall make use of a data communication channel to transmit acquired data to the base station. The software must perform the following functions:
1. Bootloader for firmware upgrades to be sent over the air. The XBee shall provide two outputs, one to reset the microcontroller and the other to indicate to the bootloader to wait for programming instructions (rather than jump directly to the application). The bootloader shall regularly test the XBee bootloader output and effect a jump to the application when it is deactivated.
2. The microcontroller application shall implement regular timed sleeps, to be woken either by an external event or after a given time. When it wakes it may wake the XBee also, and transmit a status message to the base station as part of the data connection. The XBee need not be woken if only count events are occurring.
3. The microcontroller application shall implement a command interface to allow the base station to make configuration changes.
4. For timed A/D measurements, use a timer to wake the AVR and perform A/D conversions and other polled input measurements. Configuration settings will be used to select which of these is activated, if any. It may be preferable to use the XBee to perform the analogue conversions as it has its own internal reference voltage. If no ports are identified to provide measurements, the interrupt is disabled.
5. The AVR is set to wake the XBee regularly, as required to ensure continuity of connection to network XBee routers. It will then transmit any measurements made in the interim, if any.
6. Set the watchdog timer to a given (configurable) value. When it fires, check the XBee and wake it up. Check the communication with the base station. If failures occur, reset the XBee. This may result in a NI (node identify) message being sent by the latter.
Configuration settings:
- Configure ports to convert analogue signals.
- Configure ports to read digital signals.
- Configure frequency of polled measurements.
- Enable the counter measurements by pin change interrupt.
## Remote Node Firmware Watermeter
This has a very low power requirement. Since the only measurements are counts, the firmware uses a slightly different approach for managing sleep and interrupts. See the watermeter document.
## Testing
There is only a limited debugging capability in the AVR microcontrollers so code may be verified by running it on a Linux machine and setting the AVR specific instructions to stubs. Add code to read arbitrary data from a file. Test first the parsing of the XBee messages, then the iHex lines.
Testing on the AVR itself is somewhat more challenging. First test the parsing of XBee messages by echoing back responses to an arbitrary message. Then the parsing of the iHex lines, by passing back responses before actually programming the device.
# Example System Setup
This describes an example system setup in which the base station and GUI are running on the same PC. Adapting this to a system with the base station installed on a separate machine is described at the end.
# Notes
Compile the base station software as described above. This is found in the distribution directory Xbee-acqcontrol.
Sleep Modes
The XBee cannot be contacted by the XCTU configuration software unless its sleep settings are made within certain parameters.
Apparently when pin sleep is used, the XBee will sleep immediately regardless of any transmissions waiting or in progress. This means that it must be kept awake for a time after the last transmission. This time may depend on the length of the transmission and any network protocol responses. In cyclic sleep modes 4,5 the XBee can be made to stay awake after sleep is requested. A value of 100ms to 200ms appears to be adequate. Tests show that the transmission is only a few tens of ms, so 100ms wake after sleep request would be adequate.
One solution to this would be to make use of the Tx Status frame sent back after a successful transmission. Keep awake until this comes. It is only important for the final acknowledgement, but could be used to resend the latter in case of failure.