Watermeter Design Notes
# Introduction
These are notes on the design of a watermeter data acquisition board using an AVR microcontroller and XBee communications for the Xerofill project.
The choice of this configuration was made to allow wide flexibility of data collection, management and communication. The choice of AVR was based on familiarity with the architecture, ready availability of software support tools and small device size.
The primary consideration of the project is low power consumption to maximize battery life. Extensive use of sleep modes in the microcontroller and the XBee, and careful use of power during wake periods can help to achieve this goal.
# Requirements
The process to be monitored is a pulsed signal whose characteristics determine rate of flow and quantity of water passing through the meter. The primary measure is the number of pulses counted in a given time period. The expected pattern of signal arrival is in bursts of variable length. Signal pulse rate is 400Hz maximum (2.5ms minimum pulse period).
- The AVR shall count the pulses and transmit the total to the base station.
- Signal pulses shall interrupt the microcontroller, or wake it from sleep. The wake process must be completed within 1ms.
- The microcontroller shall instruct the XBee to transmit a measure of battery voltage following the pulse count transmission.
- The XBee shall remain awake until reception of a response from the base station containing any queued messages. It shall return to sleep mode after the last of these messages have been received and answered, and no further transmission is needed.
- The microcontroller shall remain awake for 20 seconds following the last pulse. It may then sleep.
# Design Choices: Power Supply
The power source will influence the electronic circuit and PCB layout to a large extent.
The circuit requires a nominal operating voltage of 3.3V
- Xbee S2 ZB 2.1V to 3.6V
- AVR speed grade 4MHz 1.8V to 5.5V
- MAX953ESA operational amplifier/comparator 2.4V to 7V
Thus the acceptable operating range is 2.4V to 3.6V.
## AA Battery Pack 4 x 1.5V
- This will require a regulator to 3.3v.
- Supply voltage will be steady.
- Measurement of battery state will require extra components.
- Ready interchangeability of batteries among different chemistries.
AA size Alkaline batteries can provide 2800mAH, AAA size Alkaline batteries can provide 1200mAH at low current drain.
## Li Battery 3.6V
These are Lithium Thionyl Chloride.
- Supply voltage will be steady until the very end, requiring precise monitoring.
- Xbee can monitor voltage internally.
- Hazardous and may require trained person to change.
- Half AA small in size allowing simplicity of placement of components on PCB.
The possible sizes are half AA (1200mAH), full AA (2400mAH). Two AA cells can be joined via Schottky diodes. A low droput regulator may be used. The TPS77033 is specified to drop 35mV at 50mA. This will allow the battery to droop to almost 3.3V before regulation ceases.
# Design Choices: Electronics
With the aim of minimising battery power drain, the following outlines possible choices for the mode of operation of the microcontroller. The microcontroller and XBee will be placed in sleep mode during periods when no signals are arriving, to be woken up at the start of a signal burst sequence.
A major consideration is how the signal pulses may be counted (by hardware or software) and what type of sleep modes are appropriate for these devices.
A second consideration is to minimise the number of components and to ensure that they are of minimal size due to the space constraints on the PCB.
## Microcontroller
The microcontroller shall be either the ATTiny2313A or the ATTiny441 series. These are selected for their low power, small device size and availability of UART peripherals. Other ATTiny devices have a generalized form of serial communications (USI) that require additional software support to use as a USART. The ATTiny2313A lacks an A/D converter and is slightly larger in its DIL package form. For sleep modes these devices offer only idle, standby and power down, the last of which is the lowest power mode. Power down mode turns of most clocks and so allows only a limited number of external events to wake the microcontroller. The AVRs can power down unused peripherals in active mode.
## Counting Pulses
### Interrupt on Count
Interrupting the microcontroller and waking from a sleep state appears to be the best solution in terms of PCB space and power consumption. Only the microcontroller, XBee and signal conditioning electronics are needed. The microcontroller will be woken from power down mode by an arriving signal pulse. It will then count pulses by means of an interrupt service routine (ISR) and at an appropriate time it will wake the XBee and transmit the result along with a battery voltage measure. The watchdog timer may be used to perform the periodic awakening. This requires the watchdog timer clock to remain active, but this is very low frequency and hence low power drain.
### Hardware Counter
This is an alternative to the above solution. A single external counter chip with serial output would provide a lowest power solution, leaving the microcontroller and XBee to remain asleep until a burst of counts has been completed. Only one counter device has been found that has the desired features, but it has been discontinued. A major operational difficulty with this solution is how to wake the microcontroller at the optimal time.
### Timer/Counter
This is another alternative to the above solution. One of the microcontroller timer/counters may be used to count pulses directly. This requires one of the timers to remain powered on and the microcontroller to be placed in standby mode (this is the same as power down but with system clock enabled).
Standby mode consumes over 100 μA in the ATTiny441 compared to less than 1μA in power down mode. The microcontroller could be placed in standby mode after wakeup from power down. Wakeup can only occur with an external interrupt. As such the signal pulses must be applied to an interrupt pin as well as the counter input pin.
Standby mode requires a crystal clock source (not the internal RC oscillator), which means additional components on the PC board.
The datasheets do not indicate if the counters will be operational in standby mode.
It appears that using a counter is an unnecessary complication which will only result in increased power consumption during sleep phase.
## Other Considerations
### Clock Timing
Clock frequency affects power drain in active mode. The internal clock options are:
- ATTiny2313A has an internal calibrated clock with a preset divide by 8 option allowing 1MHz or 8MHz. There also appears to be a 4MHz option but this is not explained in the datasheet and it is uncertain if the clock divider applies. It also has a 128kHz low power oscillator. An additional clock prescaler is available providing division ratios up to 256 on any clock source.
- ATTiny441 has an internal calibrated clock with a divide by 8 option allowing 1MHz or 8MHz. It also has a low power oscillator with a number of frequency ranges between 32kHz and 512kHz. An additional clock prescaler is available providing division ratios up to 256 on any clock source.
In both microcontrollers the clock startup time after wake from sleep for the internal clocks is 6 clock cycles.
### USART
The USART is used to communicate serially with the XBee. A baud rate of 38400 baud causes severe constraints on the AVR clock frequency. The normal asynchronous mode will require 16 samples and the double speed mode 8 samples. This will constrain the clock frequency to be well over 1MHz. If the baud rate is reduced to 9600 a clock frequency of 1MHz can be used for the double rate asynchronous mode, or 2MHz for the normal asynchronous mode. This will give an acceptable clock error of 0.15%.
### ISR Response Time
The specified response time for an asynchronous interrupt is:
- four clock cycles to clear the Global Interrupt flag (GIF), and push the program counter (PC) to the stack.
- Two (rjmp) or three (jmp) clock cycles are needed to execute a jump to the ISR.
- Another four clock cycles is needed to return from the ISR to pop the PC, increment the stack pointer (SP) and set the GIF.
- On wake from sleep mode an additional four clock cycles is needed in addition to the clock startup time. However this occurs only once in a burst of signal pulses and may be neglected for the moment.
### ISR Code
The remaining ISR time is taken up with user code. An event counter needs to be incremented and a decision made regarding transmission of results. The actual code for initiating transmission will be external to the ISR.
All operations use 8 bit register or memory locations.
The ISR must save and restore any used registers and the status register. If one register is used this needs 6 clock cycles.
The processing instructions needed are a load from memory followed by increment and store back to memory.

ldd Rx,count_low
inc Rx
sdd count_low,Rx
This requires five clock cycles.
In addition to this a program branch instruction must be made on counter overflow. This would need to test for zero following the increment instruction.

cpi Rx,0
breq k
ldd Ry,count_high
inc Ry
sdd count_high,Ry
where k is the number of instructions to skip. This requires two clock cycles if a branch occurred, and six if the code were executed.
The average execution time for this code is therefore interrupt latency (10), sleep startup if in sleep mode (10, neglected), register save and restore (6), core code execution (7), branch execution every 256 ISR calls (6-2):
23+(6-2)/256 clock cycles
The additional execution time following a counter overflow may be extended if the counter is made longer. An absolute minimum clock frequency will be 18/2.5ms = 9.6 kHz. It can be concluded that the ISR time is negligible. This indicates that additional latency due to overflow for any one interrupt, plus the additional overhead in the C language compilation, should not result in any loss of data.
## Transmission of Results
A choice must be made when to transmit results to the base station. If the extreme choice is made that the transmission is made only when the count reaches a certain level, then the lowest power consumption will be achieved. However as the XBee is unreachable while asleep, this may cause results to be unavailable for extended periods.
If the XBee is to be woken up at regular intervals to transmit results, then either the XBee must be placed in cyclic sleep mode and wake the microcontroller, or the microcontroller must run a clock timer while asleep and wake the XBee at regular intervals. The watchdog timer can be used during power-down mode.
### XBee Sleep
The XBee specifications state a current drain of less than 1 μA in sleep mode, however it is not clear if this is modified by the activity of the timer. Some forum posts have indicated a problem with the drain being as much as 100 μA. There is a hint on the Digi Wiki that using cyclic sleep will increase power drain during sleep mode, which is expected as clocks and a timer must be active. Others hint of a mystery specification of 50 μA in cyclic sleep mode.
A note on one of the forums indicated that the sleep_rq pin be held low for “deep” sleep (deep sleep is not mentioned in the documentation to hand for the Xbee type being used). This seems counter intuitive since doing this will wake the XBee, unless the pin sleep mode is disabled.
Note: the coordinator must set the “Child Poll Timeout” to a longer time than the end devices' maximum sleep time to ensure that the latter are not removed from association while asleep.
The end device XBee has only pin wake (mode 1), cyclic sleep (mode 4) and cyclic sleep/pin wake (mode 5). In cyclic sleep modes the XBee wakes regularly. This must be set quite low (default is 200ms) in order for the configuration utility to be able to reconfigure the device.
A pin wake mode is needed for the AVR to be able to communicate its results. When the last transmission has been sent, the XBee must be allowed to remain awake for at least 100ms to allow the transmission to complete.
### AVR Wakeup
If the AVR is used to wakeup at regular intervals, the watchdog timer must be used. This increases the power down current consumption to 4 μA typical from the 0.17 μA without the timer enabled. It can be configured to interrupt rather than reset in order to wake up the AVR without loss of data.
The “Child Poll Timeout” mentioned above also applies in this case, so there is a limit on the amount of time the XBee can sleep.
Given the uncertainty about power draw by the XBee in cyclic sleep mode, it would be sensible to use pin sleep only and accept the higher drain on the AVR.
To conserve power in active mode the following unused peripherals must be turned off. For the ATTiny441 (the ATTiny2313A is similar but has fewer peripherals):
- A/D converter (not ATTiny2313A).
- Analogue comparator.
- Brown out detector (either fuse bits or by BOD-sleep).
- Internal voltage reference (automatically disabled when the above are disabled).
- Timer/counters.
- SPI.
- TWI.
- USART1 (not ATTiny2313A).
- All digital input buffers for unused I/O ports.
The USART0 will remain powered on, as well as the input buffers for INT0 and the XBee on/sleep signal.
According to the ATTiny441 and ATTiny2313A specifications the AVR will consume 400 μA for a 1MHz clock and 3.3V Vcc. The USART0 will consume 22 μA at 3.3V Vcc.
The wake time will depend on the nature of the process being measured. The AVR will remain awake as long as signals are being generated.
## XBee Wake Time
When the XBee is woken, the microcontroller will need to announce itself to the base application. This will allow the application to pass on any specific instructions to the node. The XBee network does support the buffering of application messages but only for a maximum of 28 seconds.
The microcontroller will send a packet of data for transmission to the application and wait for an acknowledgement to be received. Once the transaction is complete the XBee will be placed back in power-down mode. In most cases this simple transaction will be the only action that occurs.
There will be times where more interaction occurs if the base station requests additional status information from the node or transmits a large amount of information, such as a firmware upgrade. These can be ignored for the point of view of power drain as they will be uncommon.
As an example a data message of 10 bytes that includes four bytes of data plus six bytes of protocol framing will take about 8 ms to transmit serially to the XBee at 9600 bps. The XBee takes about 10 ms to send this and receive a response from the network. The time of response to the application message however will depend on the application and the supporting hardware, software and protocols, and will need to be measured.
In the meantime the XBee must be in a position to receive that response. In reality the response will have been buffered and it is only necessary to re-enable the receiver at some near future time. Thus the XBee will only need to be active when it is sending and receiving, and not while the application is processing the message. The Xbee could be put back to sleep and woken again after a second or so to receive any waiting messages.
Assume that a typical communication will require the XBee to be awake for only 36 ms total (as a first estimate). Current drain in active mode is 40mA for the basic XBee ZB (S2) in both transmit and receive, and 15mA while idle. If the XBee is woken once per hour for a simple transaction then the average current drain will be
40 mA * 36 ms/1 hr = 0.4 μA.
This result suggests that the assumed operational parameters above might be relaxed, for example with the Xbee being woken up every 10 minutes for an average current drain of 2.4 μA.
## Total Power Demand
The total power demand may now be estimated from the above design choices.
- AVR in power down mode watchdog timer enabled, continuous 4 μA.
- AVR in active mode with 1MHz clock, 400 μA for the CPU and USART0 22 μA for an unspecified duty cycle.
- XBee in pin sleep mode, continuous 1 μA.
- XBee in active mode, average 2.4 μA.
- IR LED 10 μA.
- Comparator 5 μA.
- Bias chain 20 μA.
- Pull down resistor 1M for Sleep_Rq, held high during XBee sleep, 3 μA.
The final current drain will depend on the amount of time the AVR is kept in active mode. If this is say 1% of the time (about 30 seconds every hour) then the total drain is 46 μA.
Measured current drain for whole circuit with AVR and XBee sleeping is 35uA.
A battery pack 2800 mAH will last for 62,000 hours (7 years).
## Hardware
The microcontroller is assumed to be any one of the Atmel AVR devices that has enough FLASH memory to hold a bootloader (which needs 2K memory). The following considers the ATMega48/88/168/328 series (excluding the ATMega48 due to its low FLASH size). These have 23 signal pins plus ground, Vcc and Aref. The following allocation of XBee and microcontroller ports should leave sufficient digital I/O and analogue Inputs for expected application needs. The AVR ports are shared with alternate functions. The ports freed for data acquisition have been selected to maximise the foreseeable needs. All these ports except for the Aref input can be used for digital I/O.
The below table shows the selected interconnections between the XBee and the AVR as well as various I/O ports available in the AVR for data acquisition.
When setting up the microcontroller, select the internal 8MHz clock; set the bootloader size to 1024 words; and set the watchdog timer to be always on. The latter will ensure that the watchdog timer is operational in a sleep state.
The selected AVR will need to use the Power Save sleep mode to ensure current drain is minimal (around 4 microamps with the WDT enabled). This means that the counters 0 and 1 will not be running. Therefore external counting will be done using interrupts that will wake the AVR and register on each count. Attempting to use a timer in this case is unreasonable.
In the circuit diagram below the 3.3V power is derived from a regulator with microamp quiescent current and a current boost transistor. Two inputs, an analogue and digital input are provided, the former could be read by the XBee directly or an A/D input in the microcontroller. The digital input is intended for counting events and is passed to a microcontroller general purpose digital port which can interrupt when the signal changes. A voltage divider for the battery monitor voltage is controlled by a MOSFET which turns off all current drain when the XBee is asleep. This can be passed either to the XBee or the microcontroller. A voltage reference for the microcontroller is derived from this, although this may be omitted if the microcontroller does not perform analogue measurements. Note that this diagram omits power supply filters needed for stability and A/D accuracy.
XBee Pin	XBee Port	Function	ATMega168 Pin
2	DOUT	UART Data Out	2 (Out PD0)
3	DIN	UART Data In	3 (In PD1)
9	CTS	Clear to send (from XBee)	4 (In PD2)
16	RTS	Request to send (to XBee)	5 (Out PD3)
9	Sleep_RQ	Wake XBee	19 (Out PB5)
13	ON/Sleep	XBee Sleep Indication	18 (In PB4)
5	RESET	Reset XBee	17 (Out PB3)
7	DIO11	MC Wake/Bootloader	16 (In PB2)
4	DIO12	Reset MC	1
6	DIO10
15	DIO5
11	DIO4
20	AD0
19	AD1
18	AD2
17	AD3
		PD4/Timer Count 0	6 (In T0)
		PD5/Timer Count 1	11 (In T1/OC0B)
		PD6/Analogue Comparator	12 (In AIN0/OC0A)
		PD7/Analogue Comparator	13 (In AIN1)
		PB0/Input Capture 1	14 (In ICP1)
		PB6	9
		PB7	10
		PB1	15 (OC1A)
		Analogue Reference	21 (In ARef)
		PC0/ADC0 Analogue In	23
		PC1/ADC1 Battery Monitor	24
		PC2/ADC2	25
		PC3/ADC3	26
		PC4/ADC4	27
		Power Off Control	28

## Firmware
With the AVR placed in power down sleep, the watchdog timer and counter interrupt are the only two events that can wake it. This gives rise to a number of difficulties.
Firstly, the counter interrupt INT0 triggers asynchronously only on low level mode when in power down mode. This raises a significant difficulty if the slotted wheel stops at a point that holds the count signal low.
The counter interrupt INT0 can be replaced by a pin change interrupt PCINT9 which is also asynchronous. This only requires then to determine the polarity of the counter signal.
The ISRs need to process an amount of information: the counter interrupt needs to determine when to increment the count, and the watchdog timer interrupt needs to initiate a transmission.
At the time the watchdog timer interrupts and wakes the AVR, a period of time is needed for the AVR to remain awake to receive incoming transmissions from the base station and take action on them.
# OptoElectronics
For the first prototype the LNJ026X8BRA1 LED and the S1133 photodiode was used.
## Photodiodes
- S1133 photodiode. 8Mm x 6mm x 1.5mm. This can be mounted as though hole or directly on the underside of the board. Physically the direct mounting leaves adequate clearance. Maximum spectral response is in the visible range, 720nm, which is midway into the red, giving 0.4A/W. The component is obsolete.
- VBPW34S photodiode. 6.4mm x 3.9mm x 1.2mm, white 430nm to 1100nm. Forward Vmax 1.3V.
- SFH2270R photodiode. 5mm x 3mm, 2.1mm high underside mounting. Maximum spectral response 560nm in the yellow. Appears to be discontinued.
- TEMD6010FX01 photodiode. 4mm x 2mm x 1.05mm, visible range 430nm to 610nm with smaller peak at about 890nm in the IR.
## LEDs
- SFH4056 through-hole or surface mount IR. 1.7mm by 3.3mm, 1mm height, 0.7mm through hole. Peaks at 850nm. Appears to be discontinued.
- SFH4258 surface mount IR. 3.4mm by 3.0mm. 3.5mm height. Through hole mounting requires precise hole diameter. Peaks at 850nm.
- LNJ026X8BRA1 white bright. 1.6mm by 0.8mm, 0.35mm height. About 40mcd at 5mA white, that is, spread over the spectrum. Appears to be discontinued.
- OP280PS LED SMD. Infrared. 2.2mm by 3.5mm, 2mm height. Peaks at 850nm. Appears to be discontinued.
- VSMY2850 through-hole Infrared. 2.2mm by 2.2mm. 2.8mm height, 1.2mm through hole. Peaks at 850nm.
- APD3224ZGC-F01 3.2mm x 2.4mm green clear SMD. Peaks at about 520nm with 1900mcd at 20mA. Appears to be discontinued.
- LOT77K-LIM2-24-Z LED top-led 6mm x 2.6mm orange 606nm SMD. 11...28mcd at 5mA. Appears to be discontinued.
## Detection
The photodiode current is passed through a BJT with a 270K collector resistor and hence to a MAX952 comparator with a 1M positive feedback resistor. The source resistance of the resistor network is about 135K (270K paralleled with an equivalent value from the BJT to reach the reference voltage 1.2V). The 3.3V high output from the comparator will then add an additional 300mV which will be the hysteresis range, that is the input signal will trigger at 1.2V on the rising edge and 0.9V on the falling edge.
# Other Considerations
## Power Supply Voltage
The MAX953 or MAX954 operational amplifier/comparator combination will work down to 2.4V, while the AVR will work down to 1.8V and the XBee to 2.1V.
The LED may require a higher voltage. At 20 μA it will drop about 2V leaving little margin for controlling current if the battery voltage drops.
## Board Layout
### Components
Apart from the Opto components, the following packages are needed for the integrated circuits:
- ATTiny4313. SOIC 10mm x 13mm. VQFN 3mm x 3mm.
- ATTiny841. SOIC 8.5mm x 6mm. VQFN 3mm x 3mm.
- TPS77033. DBV package 3mm x 3mm.
- MAX952ESA. SO-8 package 5mm x 6mm.
- S9014 BJT.
### PCB
The PCB needs attention to the physical structure.
- PCB diameter 58.5mm.
- Copper diameter 52.5mm.
- Web fingers 10.5mm long , 8mm high.
- Central area between web 37.5mm diameter.
- Disk diameter 30mm, slots 4mm long, 1mm from rim.
- Magnet holder 11mm diameter.
- Shaft 5.5mm with PCB hole at 8.5mm for inserted grommet with 6mm hole.
LED mount must be placed between the web fingers and the magnet holder, outer diameter 36mm, inner diameter 12mm. This leaves only 6mm at the rim for mounts to pass between the LED mount and the main PCB.
The LED must be mounted at the point 12.5mm from the centre. The supports could be stiff wire soldered at three points. Alternatively thin bolts alternating with stiff wire acting as spacers. Separation of boards 5mm.
## Components
Package sizes for passives “metric 2012 (imperial 0805)” minimum to ease manual handling.
Schottky diodes are proposed for combining dual batteries in parallel. Most diodes available however either have high forward current and consequently large package, or have a forward voltage that is too high. As a result only one battery connection will be provided until a suitable device is found.
- Resistor. Eg SUSUMU - RR1220P-333-D - RESISTOR, THIN FILM, 33KOHM, 100mW, 0.5%, metric 2012 (imperial 0805).
- Electrolytic Tantalum capacitor eg VISHAY SPRAGUE - 293D106X9016A2TE3 - CAP, TANT, 10UF, 16V ESR 3 ohm metric 3216 (imperial 1206).
- Ceramic capacitor eg AVX - 08051C104JAT2A - CAP, MLCC, X7R, 100NF, 100V, metric 2012 (imperial 0805).
- Inductor eg COILCRAFT - 0805PS-102KLC - INDUCTOR, PWR, 1UH, 1.6A, 10%,340MHZ, metric 2012 (imperial 0805). Not used at this stage.
- ATTiny4313. SOIC 20S2 package.
- XBee package 20 pin DIL length 27.61mm, width 24.38mm, pin row spacing 22mm, 0.51mm pins spaced at 2mm (total length 18mm).
- BJT. The S9014 appears to be difficult to find. We need an equivalent with 3 lead package style SOT-23.
- MOSFET eg NXP - PMBF170,215 - MOSFET, N, SOT-23.
- Op Amp package style 8 pin. Eg the LM158 available as M08A. The MAX952ESA is available as 8-SOIC (SOIC-8?).
- The regulator TPS77033 has a 5-lead SOT-23 (rj-5) package.
- The programming connector should be a 6 pin header, 2mm pitch, eg MOLEX - 87758-0616 - HEADER, SQUARE PIN, M/GRID, 6WAY, or a socket style connector. A possible matching line socket connector might be JST (JAPAN SOLDERLESS TERMINALS) - 06P-SJN - HOUSING, RECEPTACLE, CRIMP, 2MM, 6WAY.
- The XBee adaptor is used if the XBee is mounted on a separate board and need not be an actual connector. It could be mounted over the area set aside for the on-board XBee.
## AVR Pin Allocations
### ATTiny4313
Tentative Pin Allocation ATTiny4313
1. PA2 - RESET (pullup with capacitor for power-on reset)
2. PD0 - RXD from XBee
3. PD1 - TXD from XBee
4. PA1 - CTS
5. PA0 - RTS
6. PD2 - INT0 level interrupt from counter (wakeup)
7. PD3 - Test output
8. PD4
9. PD5 - Battery Measurement Control
10. GND
11. PD6
12. PB0
13. PB1 - Xbee On/Sleep
14. PB2 - XBee Reset
15. PB3 - XBee Sleep_Rq
16. PB4 - Bootloader enable
17. PB5 - MOSI (for firmware load)
18. PB6 - MISO (for firmware load)
19. PB7 - SCK (for firmware load)
20. VCC (1.8V to 5.5V)
### ATTiny841
Tentative Pin Allocation ATTiny441/841
1. VCC (1.7V to 6.0V)
2. PB0 - Bootloader enable
3. PB1 - INT0 level interrupt from counter (wakeup)
4. PB3 - RESET (pullup with capacitor for power-on reset)
5. PB2 - XBee Reset
6. PA7 - Battery voltage enable
7. PA6 - (MOSI)
8. PA5 - (MISO)
9. PA4 - (SCK)
10. PA3 - XBee Sleep_Rq
11. PA2 - RXD0 from XBee
12. PA1 - TXD0 to XBee
13. PA0 - Xbee On/Sleep
14. GND
## Tests
These tests operate various scenarios to measure the power drain. ATTiny4313 was used.
### AVR active, all peripherals off
- 1MHz clock, 400 μA at 3.3V supply voltage. Agrees with datasheet.
- 1MHz clock, USART powered on, not in use, 411 μA.
### AVR Sleeping, Watchdog Timer Enabled
4.6 μA at 3.3V supply voltage, agrees with datasheet.
### AVR Sleeping with 400Hz Signal Wakeup
The watchdog timer is set to wakeup at maximum time, 8 seconds. The active AVR then sleeps again until 10 seconds has elapsed (this will be made configurable).
A continuous 400Hz signal, representing the maximum signal rate, draws 7 μA at 3.3V supply voltage. This includes wake from sleep with both WDT and interrupt, and a small test on the signal counter and the WDT counter. Current at 5V supply is 12.9 μA.
## XBee Compatibility
Some XBee networking modes are incompatible with Zigbee devices.
From https://www.sparkfun.com/pages/xbee_guide these different devices are:
- XBee Series 1. Point-point. Incompatible with other series.
- XBee ZNet Series 2.5. Now obsolete.
- XBee ZB (Series 2). Currently being used. hardware same as ZNet Series 2.5.
- XBee 2B. Improved hardware. Same as ZB firmware.
- XBee 900MHz. Runs either point-multipoint or Digimesh.
- XBee XSC. Same as 900MHz but longer range,lower datarate.
- XBee XSC S3B. Higher power version.
The XBee ZB firmware is based on the EmberZNet 3.x ZigBee PRO Feature Set mesh networking stack, while the XBee ZNet 2.5 firmware is based on Ember's proprietary "designed for ZigBee" mesh stack (EmberZNet 2.5.x).
## Xbee Settings
All MACs start with 0013A200.
		MAC	BAUD	SM	SN/SP	ST	SO
Coordinator		4089DEBC	38600	0	B50/AF0	-	0	Whip
Coordinator		408B4B30						Whip
Router 1		408B4B82	38400	0	B50/AF0	-	0	Whip
End 2		4089DECC	9600	5	B40/AF0	1F4	6	Whip
End 3		4079A7D7	9600	5	1/300	128	2	Whip
Router 4		4094570A	38400	0	B50/AF0	-	0	Whip
Router 5		408B2CF3	38400	0	B50/AF0	-	0	Whip
Router 6		408B2D12	57600	0	B50/AF0	-	0	Whip
Router 7		408B2CF4						Whip
End 8		407675D3	9600	5	1/300	128	2	SMA
Router 9		4089DED8	38400	0	B50/AF0	-	0	Whip

SM is sleep mode 0=never sleep, 1=pin sleep, 4=cyclic sleep, 5=cyclic/pin sleep
SP is sleep period in 10ms steps.
SN is number of sleep periods multiplier.
ST is time in ms before sleep: time to stay awake after sleep requested.
SO is sleep option bits 1=stay awake whole ST time, 3=enable extended sleep.
# Equipment
The equipment available for prototype testing:
- (2) Seeed Xbee-USB adapter ID 0403:6001 FTDI FT232 USB-Serial.
- ICStation Xbee-USB-RS232 adapter ID 0403:6001 FTDI FT232 USB-Serial. Serial connections at 5V levels plus 5V, GND and RST intended for Arduino connection.
- (2) Xbee-Arduino shield by TinyOS.
- Xbee-Arduino shield by Funduino.
- (2) Seeed XBee carriers. (2) Grove system XBee Carriers. These are mounted with adjustable analogue input. 3.3V power, no regulator.
- (2) Prototype boards with ATMega48 and adjustable analogue input. Regulator for 5V and above.
- Prototype board with MAX232 serial adapter. Regulator for 6V and above.
# Notes
Interference
The XBee transmissions produce an analogue pulse on the photodiode/amplifier circuitry when the photodiode is turned on. The origin of this pulse is uncertain but may be as early as the photodiode itself. A CRO probe placed on the photodiode output (BJT input) reduced the interference by eliminating a short pulse from the cyclic wake, and leaving only the longer data transmissions to interfere. Any external ground connection such as a CRO lead also increased the interference. The introduction of a current sense resistor of 10Ω also increased the interference. This may be coming through the power supply despite the use of a regulator.
Replacement of the XBee (whip antenna) with an SMA version plus external aerial seems to have reduced the interference. Possibly a metal cover connected to the SMA ground could help.
End Device
- ND node discovery options 3 (bit 0 append DD value to node response, and bit 1 local device responds to node discovery command).
- NH number of hops set to 1E.
- JN join notification set to enabled.
- DIO7 set to disable CTS.
- SM set to 5, ST set to 120, SP set to 300 (7.68 s), SN set to 1, SO set to 0.